## Slide 1
SHIP DESIGN
GROUP 3
ENGINEERS
Breno Guedes Gallo
Marcos Vicente Soares Pifano
Thiago Aguiar Lima
Poli
marine
OIL TANKER
São Paulo, 20th of October of 2023

## Slide 2
Poli
marine
1. SHIPOWNER REQUIREMENTS
2. FIRST ESTIMATES
3. WEIGHTS AND CENTERS
4. SPACE AND ARRANGEMENT
5. STABILITY
AGENDA
PNV3415 – Project of Ships

## Slide 3
PRODUCT
CRUDE OIL
REQUIREMENTS
SHIP OWNER
Poly
marine
AUTONOMY
6,000 NAUTICAL MILES
DEADWEIGHT CARGO
115,500 TONS
ROUTE
ALGERIA - USA/HOLLAND/UK
SPEED
15.7 KNOTS
4
DRAFT 11

## Slide 4
ARZEW PORT
PORT OF VIRGINIA
It has the Norfolk Naval base. The largest ship that ever docked in the port was 396m long.The draft maximum is 15.24m.
PORT OF ROTTERDAM
The port has the capacity to accommodate ULCC type oil tankers, supporting adraft of up to 22.55m.
PORT OF MILFORD HAVEN
Located in Wales, the channel exceeds 17m in all tidal states.The maximum draft is 16.1m to dock.
Algeria is the largest producer of crude oil in the African continent, and a member of OPEC since 1961.Arzew is a medium-sized port with the following restrictions:
Maximum draft of 14.5 m
Maximum LOA of 300 m
Maximum DWT of 181,433 tons
5

## Slide 5
SHIP CHARACTERISTICS
AFRAMAX CLASS
6
CARGO CHARACTERISTICS
ALGERIAN CRUDE OIL
Products
refined
Products
Refined
Or oil
crude
Oil
crude
Source:
MAIN SYSTEMS OF AN OIL TANKER:
Cargo pumping systems;
Tank cleaning systems;
Tank ventilation and inert gas systems;
Ballast system.
The density of oils is measured by its API gravity, which is classified as follows:
• Light: Less than 870 kg/m³ (more than 31.1° API) Mediterranean
• Medium: 870 to 920 kg/m³ (31.1° API to 22.3° API)
• Heavy: 920 to 1000 kg/m³ (22.3° API to 10° API) Venezuela
• Extra Heavy: More than 1000 kg/m³ (less than 10° API)
Oil field of Hassi Berkine
820 kg/m³ (42°API)
MAIN CARGO CONCERNS:
Risk of explosion;
Risk of spillage.

## Slide 6
SPIRAL OF
PROJECT
7
Poly
marine

## Slide 7
Poli
marine
1. SHIPOWNER REQUIREMENTS
2. FIRST ESTIMATES
3. WEIGHTS AND CENTERS
4. SPACE AND ARRANGEMENT
5. STABILITY
AGENDA
PNV3415 – Project of Ships

## Slide 8
SIMILAR SHIPS
DATABASE
9
REFERENCES
OF SHIPS

## Slide 9
SIMILAR SHIPS
10
REFERENCES
OF SHIPS
390 SHIPS
1537 SHIPS

## Slide 10
SHIP
SIMILAR
11
• LOA: 249.85 m
• LBP: 239 m
• Breadth: 44 m
• Depth: 21.3 m
• Draft: 15 m
• Speed (75% MCR): 14.5 knots
• Cargo capacity: 124.9 k m³
• DWT (design): 109.5 k tons
BUILT IN
SOUTH KOREA

## Slide 11
DIMENSIONS AND
COMPARTMENTS
12
B
d
Load
Load
Load
Load
Load
Load
B
Load
Load
Load
Load
Load
Load
Load
Load
Load
Load
Load
Load

## Slide 12
METHODOLOGY
FIRST ESTIMATES
13
Analysis of DWT scatter and correlation plots by main dimensions (LBP, B, D and d);
Verification of patterns and possible regressions;
Data processing (local analysis and outlier removal);
Verification of the infeasibility of regression in the local analysis;
Calculation of descriptive statistics (main and dimensionless dimensions).
ANALYSIS OF
DATABASES
COMPARISON
OF OTHERREFERENCES
Main dimensions from the report of theUniv. of Denmark (Kristensen, 2012)and its database;
Dimensionless byShip Design and Construction (Parsons, 2003).

## Slide 13
DIMENSIONS MAIN
Local analysis: Added the two databases, analyzing ships between 105,000 tons and 126,000 tons DWT
(+/- 10,500ton of the requirement).
Total of 331 similar ships.
14
390 ships
(DWT from 62,500 to 321,000)
1537 ships
(DWT from 525 to 441893)

## Slide 14
DIMENSIONS MAIN
Linear regression: tanker ships of various sizes. Although there is a linear regression (note the low r²), only the deadweight range required by the shipowner will be analyzed.
15
Hans Otto
Kristensen
LBP from 232 to 245, with a typical value of 239.
B from 42 to 45, with typical values of 42, 43 and 44.3
D from 20.8 to 23.5, with typical values from 21 to 22.
d from 14.5 to 15.7.
CB from 0.81 to 0.85, with a typical value of 0.84.

## Slide 15
46
VCG Loaded |  | 
Component | Position (m) | Weight (ton)
Lightweight | 12.05 | 22,866.21
Total deadweight | 12.74 | 116,779.21
Total | 12.63 | 139,645.41
LCG loaded |  | 
Component | Position (m) | Weight (ton)
Lightweight | 112.43 | 22,866.21
Total deadweight | 131.70 | 116,779.21
Total | 128.55 | 139,645.41
VCG Ballast |  | 
Component | Position (m) | Weight (ton)
Lightweight | 12.05 | 22,866.21
Total deadweight | 11.46 | 58,090.26
Total | 11.62 | 80,956.47
LCG ballast |  | 
Component | Position (m) | Weight (ton)
Lightweight | 112.43 | 22,866.21
Total deadweight | 134.80 | 58,090.26
Total | 128.48 | 80,956.47
CENTER OF GRAVITYIN TWO CONDITIONS
LOADED:
  This condition implies maximum draft;
  Preferabletrim close to zero.
BALLAST:
  This condition implies minimum draft;
  If there istrim, preferable >0;